## Slide 1
DEPARTMENT OF COMPUTER SCIENCE

## Slide 2
UNITY UNIVERSITY DEPARTMENT OF COMPUTER SCIENCE | 
Course Title | SYSTEM AND NETWORK ADMINISTRATION
Degree Program | BSc. Degree in Computer Science
Course Code | COSC 4081
Credits/Contacts | 3/4
Prerequisite | COSC3052, COSC3081
Semester | SEMESTER I Year 4
Status of Course | Compulsory
Course Objectives and Competences to be acquired | After a successful completion of this course, students will be able to: Support any system administrative tasks independent of platforms; Create and administrative architecture for a network; Install and monitor important services for large systems; Understand and implement secured systems; Troubleshoot and maintain system problems.

## Slide 3
Course Description | This course introduces students to the concept of system support. It provides architecture based platform independent discussion of administrative tasks with practical architecture examples from the different platforms. The course covers a wide range of supporting tasks from personal computer management to network administration. The course is intended to provide a scalable and concrete background on system administration activities. It mainly concentrates on practical sessions to demonstrate network tasks..

## Slide 4
 | Course Content
 | UNIT ONE: INTRODUCTION TO NETWORK ADMINISTRATION 1.1 Overview of Computer Network OSI layers, Addressing, Naming and Sub-netting, Windows network concepts Workgroups, Server Domain, LDAP, Active Directory System and Network Administration System and Network Administrator and its responsibilities CHAPTER TWO: WORKSTATION SUPPORT AND SERVER HARDWARE Workstation Workstation Processor and Memory Workstation Storage and Compatibility Reliability Servers Hardware Hardware Reliability and LAN Hot Swappable Multiple Power Supplies UPS Asymmetric Multiprocessing, Symmetric Multiprocessing

## Slide 5
 | Unit Two----Continued
 | Desired Characteristics of Server: Processor and Storage Requirement CD-ROM Storage Technology Bus and Memory Technologies Reliability Fault Tolerant Feature for Servers Server Selection (10 Users, 25 to 50 Users, 100 to 250 Users, 500 to 1000 Users, 1000+ Users Server Performance in Web Page Requests Per Second Server Performance in Megabits Per Second Server Performance in Transactions Per Second Page Requests: Single Vs. Dual Server Performance in Web Page Requests Per Second Server Performance in Megabits Per Second Server Performance in Transactions Per Second Page Requests: Single Vs. Dual

## Slide 6
 | Throughput: Single Vs. Dual Transactions: Single Vs. Dual An Investigation on the Design of Scalable Servers Growth of Internet Hosts, Growth of Web Servers, Growth of Server Platforms Why do We Need a Large-Scale Server Examples of large-scale servers Caching/Proxy Servers Characteristics of Scalable Servers How to Scale a Server Up Identifying bottleneck or limitation Improving Server Scalability Design Issues The Generic Scalable Server Model Server Load Collection Request Dispatcher Domain Name Mapping (Round-Robin DNS, Smart DNS) Connection Routing

## Slide 7
 | How to Provide Single Server Image Selecting an Appropriate Server Round-robin or random Server load/capacity Location of client/server Location of resources/services The NCSA Scalable WWW Server The Berkeley Smart Client The Smart DNS
 | UNIT THREE: NETWORK OPERATING SYSTEM (NOS) Network server software Network client software Microsoft Windows NOS Features Client support Interoperability Authentication

## Slide 8
 | Unit Three---continued
 | Directory structure File and print services Application support Security Novell NetWare NOS Features, Client support, Interoperability, Authentication, Directory structure, File and print services, Application support and Security Overview of UNIX/Linux NOS Features, Client support, Interoperability, Authentication, Directory structure, File and print services, Application support, Security Macintosh NOS Features, Client support, Interoperability, Authentication, Directory structure, File and print services, Application support, Security

## Slide 9
 | UNIT FOUR: NETWORK RESOURCES AND SERVICES Network resources, Network Services Remote Administration and Access Services Directory Services, Other NOS Services
 | UNIT FIVE: INTERNET WORKING MANAGEMENT Internetworking basics Collision domain Broadcast domain Network segmentation How bridges, switches, and routers are used to physically segment a network How routers are employed to create an internetwork Internetworking Models (three-Layer Hierarchical Model) The Core Layer The Distribution Layer The Access Layer

## Slide 10
 | UNIT SIX: WINDOWS SERVER AND SERVICES Installing Windows Sever 2012 and above Active Directory Directory Services Benefits of Active Directory Domains Overview DNS and DNS Services Managing DNS Server Options, Forward lookup zone, Reverse Lookup Zone, Changing the Properties of a Zone Configuring DNS Forwarding, Conditional Forwarders, DNS Server Roles, Integrating DNS with DHCP, Implementing Dynamic DNS, Integrating DNS and Active Directory, Monitoring DNS DHCP Services DHCP Services Overview DHCP Lease Process DHCP Clients and Leases DHCP Server Configuration

## Slide 11
 | Unit Six---continued
 | DHCP Scopes Manage Reservations and Reserved Clients Verifying DHCP Reservation Configuration Integrating DHCP with Active Directory DHCP Servers Authorization Manage DHCP Options Manage DHCP Databases Managing and Configuring DHCP Relay Agent Using Multiple DHCP Servers Integrating DHCP with DDNS Troubleshooting DHCP FTP Services Overview of FTP Services FTP Objectives Configuring FTP Services

## Slide 12
 | Unit Six---continued
 | IIS Services Overview of IIS Services IIS Configuration Setting the web services Set the IP Address Website Properties
 | UNIT SEVEN: IP ROUTING CONFIGURATION Basic Access Control Lists Cabling a Network and Basic Router Configuration Managing Device Configuration Managing Switch Operating System and Configuration Files Router Configuration Static Route Configuration DHCP and NAT Configuration RIP Configuration EIGRP Configuration

## Slide 13
 | Unit Seven---continued
 | OSPF Configuration Configuring Wireless LAN Access Investigating the Routing Table Lookup Process
 | UNIT EIGHT: NETWORK TROUBLESHOOTING FUNDAMENTALS Troubleshooting Steps (hardware tools, software tools) Building a fault tolerant system. Fault Tolerant Components Fundamentals of Fault Tolerance Fundamentals of Coding Theory Fault Tolerant Schemes Industry Practices Fault-Tolerant Design Faults(Permanent Faults, Temporary Faults) Redundancy(Time Redundancy, Hardware Redundancy, Information Redundancy)

## Slide 14
 | Unit Eight---continued
 | System Failure Rate Reliability Mean-Time-to-Failure (MTTF) Repair Rate and MTTR Fault Tolerance Implementation Sever Based Implementation of Fault Tolerance Level 1=> duplicate FAT Level 2=>duplicate sever HD Level 3=> duplicate server RAID Storage: The Practical Implementation Network Operating System Support for Reliability (Striping, Parity, Mirroring)

## Slide 15
Teaching and learning Methods | Lecture Laboratory, Practical work and Simulation
Assessment/Evaluation and Grading System | Theoretical Tests (20%) Assignment (15%) Practical test (15%) Final Exam (50%)
Text Books | Limoncelli, Thomas A., Christina J. Hogan and Strata R. Chalup The Practice of System and Network Administration, Second Edition, Addison-Wesley Professional, 2007,
Reference Materials | Nemeth, Evi, Garth Snyder, Scott Seebass and Trent Hein UNIX System Administration Handbook (4th Edition), Prentice Hall, 2010 Windows Server 2012 Unleashed eBook: Rand Morimoto, Michael Noel, Guy Yardeni, Omar Droubi, Andrew Abbate, Chris Amaris,2012 Basic Router Configuration procedures for Cisco 3900 series, Cisco 2900 series, and Cisco 1900 series integrated services routers (ISRs).

## Slide 16: UNIT ONE
INTRODUCTION TO NETWORK ADMINISTRATION

## Slide 17: 1. 1. Overview of Computer Networks-----
Old paradigm:
  A single powerful computer serving all the needs of an organization
  Sneaker net --Method of sharing data by copying it to a disk and carrying it from computer to computer
New paradigm
  Computer networks: a large number of separate (autonomous) but internetworked (being able to exchange information) computers doing the job
    Merging of computer and communications technologies – no geographical barrier
    Connection:
    copper wire, fiber optics, microwaves, infrared, communication satellites, …

## Slide 18: 1. 1. Overview of Computer Networks-----
A computer network is an interconnected collection of autonomous computers
  Interconnected meaning two or more computers have the,
  ability to exchange information and sharing resources using
  some transmission media
  e.g., copper cabling, fiber optics, or radio wave and etc.
  Autonomous meaning where no one computer controls any other computer (i.e. no computer can forcibly start or stop another computer)
  Computers can be PC’s, workstations, server computers and internetworking devices such as hubs, switches and routers
  The computers can be geographically located anywhere

## Slide 19: 1.1.1 Application or uses of Computer Networks
 | Application | Descriptions and Examples
1 | Resource Sharing | Hardware( Computing resources, disks, printers…) Software (Application software, mainly databases on central servers),
2 | Communication | e-mail, newsgroups, chat room, Internet telephony, writing a report together by making changes on an online document videoconferencing
3 | Home Applications | User-to-User Communication, Entertainment, E-Commerce,
4 | Business Applications | business to business - placing orders, … business with consumers–home shopping

## Slide 20: 1.1.1 Application or uses of Computer Networks-----
 | Application | Descriptions and Examples
5 | Social Media | It helps people in getting news, feed, current trending topics of all types, etc.
6 | Access to Remote Information | It helps in accessing remote information from the end-users. For Example, details required for train tickets, plane tickets, etc
7 | Cloud Computing | Facilitated the development of cloud computing, which allows users to store and access data and applications from remote servers via the internet.
8 | Virtualization | Allows multiple virtual machines to run on a single physical machine, improving resource utilization and reducing costs.

## Slide 21: 1.1.1 Application or uses of Computer Networks-----
 | Application | Descriptions and Examples
9 | Online Education | Providing online learning platforms, distance education, and virtual classrooms.
10 | Remote Working | Allowing employees to work from home or other locations outside of the office. Especially important during the COVID-19 pandemic.
11 | E-commerce | Facilitated the growth of e-commerce by allowing businesses to sell their products and services online and reach a global market.

## Slide 22: 1.1.1 Application or uses of Computer Networks-----
 | Application | Descriptions and Examples
12 | Real-time Collaboration | Networking technologies enable real-time collaboration, allowing people to work together on projects and share information in real-time, no matter where they are located.
13 | Telemedicine | Networking technologies have also enabled telemedicine, allowing doctors and healthcare providers to provide remote medical consultations and diagnosis to patients in remote locations.

## Slide 23: 1. 1.2 Limitations of Networks
  Security Issues
  Data & information held on a network is open to many people across the world, and can easily be accessed illegally.
  In addition, when information is sent over the network from one place to another,
  it can be tapped or listened to by unauthorized parties.
  This is leads to the danger of important and
  sensitive information fall on the hands of hostile party
Virus and Malware
Networking can lead to the spreading of viruses to
another computer through the network.

## Slide 24: 1. 2.1 Limitations of Networks------
2. High initial cost
The initial cost of buying network hardware & software is very high.
3. Moral and cultural effects
Large networks such as the Internet have chat rooms and messaging services.
These enable underage children to meet peers and adults on the net, some of whom may have bad intentions.
Access to pornographic and other negative material on the Internet has made the fight against social problems such as
HIV/AIDS, bad sexual behaviour, and drug abuse more complicated.

## Slide 25: 1. 2.1 Limitations of Networks------
4. Spread of terrorism and drug trafficking
The Internet makes it easy for terrorists and drug traffickers to operate.
This is because; they use information networks for their business communications.
5. Over-reliance on networks
Most organizations have done away with manual operations.
This means that, all business processes, and the society depend on computer networks.
Therefore, if by any chance the network fails or goes down, then many systems in the society will stop working.

## Slide 26: 1. 2.1 Limitations of Networks------
6. Management of the network
Management of the Network is quite difficult as it requires highly qualified and skilled persons to handle that large network.
It requires training of people who are employed in this work.

## Slide 27: 1.2 The OSI Reference Model
OSI is an acronym for Open Systems Interconnection.
The term “open” denotes the ability to connect any two systems which conform to the reference model and associated standards.
The International Organization for Standardization (ISO) created the OSI model in 1984.
It is now considered the primary Architectural model for inter-computer communications.
The Open Systems Interconnection (OSI) reference model is a descriptive network scheme.
It ensures greater compatibility and interoperability between various types of network technologies.

## Slide 28: 1.2 The OSI Reference Model-----
The OSI model refers to a standard model used to describe the
flow of information from one computing device to another operating in a networking environment.
The model defines a set of rules and requirements for data communication and
interoperability between different devices,
products, and software in a network infrastructure
The OSI model describes how information or data makes its way from application programmes
(such as spreadsheets) through a network medium (such as wire)
to another application programme located on another network.

## Slide 29: 1.2 The OSI Reference Model-----
The OSI reference model divides the problem of moving information between computers over a network medium into
SEVEN smaller and more manageable layers,
each specifying particular network functions.
This separation into smaller more manageable functions is known as layering.

## Slide 30: 1.3 Why does the OSI model matter?
Establishing standard communication protocols is key to formalizing communication across internal and external networks such as the cloud or the internet.
Such standardization facilitates faster communication between devices and networks,
irrespective of the data resides, where it is sent, or from where it is received.
The OSI model allows equipment manufacturers to define their standards and protocols while maintaining interconnectivity with other manufacturers.
Moreover, the OSI model is key to troubleshooting network devices.

## Slide 31: 1.3 Why does the OSI model matter?
The OSI model matters because it provides a conceptual framework for
understanding how networks operate and communicate.
Here are some key reasons why it is important:
Standardization
The OSI model establishes a standard for network communication.
It divides the complex task of network communication into
seven manageable layers, each responsible for specific functions.
This standardization allows different vendors and developers to
create compatible network devices and
software that can interoperate seamlessly.

## Slide 32: 1.3 Why does the OSI model matter?-------
2. Layered Approach
The layered approach of the OSI model promotes modular design and development of network protocols and hardware.
Each layer handles a specific aspect of the communication process,
such as addressing, data packaging, error control, and flow control.
This division simplifies network design, troubleshooting, and maintenance.
3. Common Language
The OSI model provides a common language that network engineers and developers can use to discuss, analyze, and troubleshoot network functionality.
It helps in pinpointing where issues may arise within the communication process and facilitates effective collaboration among different teams.

## Slide 33: 1.3 Why does the OSI model matter?-------
4. Educational Tool
It serves as a fundamental educational tool for teaching network concepts.
By understanding the OSI model, students and professionals can
grasp the particulars of network communication and gain insights into
how different protocols and technologies fit together.
5. Interoperability
The OSI model's emphasis on standardization and layer-specific
functions ensures that networks built by
different vendors can interoperate smoothly.
This interoperability is crucial in today's interconnected world where devices and systems from various manufacturers need to communicate effectively.

## Slide 34: 1.3 Why does the OSI model matter?-------
6. Evolution and Adaptation
While the OSI model itself may not be directly implemented in modern networks (TCP/IP being the dominant protocol suite), its principles and concepts have influenced the development of network protocols and architectures.
It continues to provide a foundational understanding that guides the
evolution and adaptation of networking technologies.
In summary, the OSI model matters because it defines a structured approach to network design, communication, and troubleshooting.
It has played a pivotal role in the development and standardization of networking protocols, facilitating global communication and connectivity.

## Slide 35: 1.4 How the OSI model works?
The OSI model works by segmenting all transmitted data through a
seven-layer abstraction in order to more efficiently and securely parse and deliver the data to its destination.
To better understand this process, here’s an example of the OSI model’s abstraction process in operation.
Let’s say you decide to send an email from computer (A) to computer (B).
Email application client resides on layer 7. When you send the email,
the layer 7 application protocol encapsulates or places a header on your messages and sends it to layer 6.
Layer 6 compresses the data, encrypts the data and transfers it to layer 5.
Notes: Parse-To split (a file or other input) into pieces of data that can be easily manipulated or stored

## Slide 36: 1.4 How the OSI model works?----
Layer 5 opens a session between your computer and the outgoing server.
It also decides which data packet belongs to which file.
Finally, it adds an appropriate header and transfers the data to layer 4.
When layer 4 receives data from layer 5, it segments it and assigns each segment a destination and source port number to
ensure the data gets delivered to the correct service.
Layer 4 also enforces security controls.
Layer 3 breaks the data into packets and transmits it over multiple paths.
The packets contain destination and source IP addresses for easier identification of end devices.

## Slide 37: 1.4 How the OSI model works?
Then the data is sent to layer 2, where the DLL adds MAC addresses to the packets, which are then grouped into frames.
To deliver to the correct destination, the LLC sublayer adds control information to each frame.
Finally, the frames are transmitted to layer 1 in the form of 1s and 0s.
That binary data is then transferred to device B either through
electric pulses (Ethernet), radio waves (Wi-Fi), or light pulses (Fiber optics).
Layer 1 ensures bit synchronization so that,
as the data reverses its abstraction through each layer at the destination,
the end user receives the information in a readable format--just as it was intended.

## Slide 38: 1.5 How the OSI model works?------
The physical layer is responsible for movements of individual bits from one hop (node) to the next.

## Slide 39: 1.6 The Seven OSI Reference Model Layers
The process of breaking up the functions or tasks of networking into layers reduces complexity.
Each layer provides a service to the layer above it in the protocol specification.
Each layer communicates with the same layer’s software or hardware on other computers.
The lower 4 layers (transport, network, data link and physical —Layers 4, 3, 2, and 1) are concerned with the flow of data from end to end through the network.
The upper three layers of the OSI model (application, presentation and session—Layers 7, 6 and 5) are orientated more toward services to the applications.
Data is Encapsulated with the necessary protocol information as it moves down the layers before network transit.

## Slide 40: Layer 7: Application Layer
The application layer is the OSI layer that is closest to the user.
It provides network services to the user’s applications.
Contains all the higher level protocols that are commonly needed by users; examples:
    HTTP (Hypertext Transfer Protocol)
      It is the basis for the WWW - when a user use a browser and the browser wants a Web page, it sends the name of the page it wants to the server using HTTP; the server then sends the page back
    TELNET - virtual terminal, to log on to a remote machine
    FTP - file transfer
    SMTP - e-mail
    DNS - for mapping host names onto their network addresses

## Slide 41: Layer 6: Presentation Layer
The presentation layer ensures that the information that the application layer of one system sends out is readable by the application layer of another system.
If necessary, the presentation layer translates between multiple data formats by using a common format.
Provides encryption and compression of data.
Examples :
JPEG,
MPEG,
ASCII,
EBCDIC, HTML.

## Slide 42: Layer 5: Session Layer
The session layer defines how to start, control and end conversations (called sessions) between applications. This includes:
Control and management of multiple bi-directional messages using dialogue control.
keeping track of whose turn it is to transmit
Synchronizes dialogue between two hosts' presentation layers and manages their data exchange.
preventing two parties from attempting the same critical operation at the same time
Offers provisions for efficient data transfer.
check pointing long transmissions to allow them to continue from where they were after a crash. Examples :- SQL, ASP(AppleTalk Session Protocol).

## Slide 43: Layer 4: Transport Layer
The transport layer is responsible for process-to-process delivery of the entire message.
A process is an application program running on a host.
The transport layer, ensures that the whole message arrives intact and in order, overseeing both error control and flow control at the source-to-destination level.
The Transport layer also encompasses to enables multiple applications to communicate over the network at the same time on a single device
Layer 4 protocols include:
TCP (Transmission Control Protocol) and UDP (User Datagram Protocol).

## Slide 44: Responsibilities of Layer 4: Transport Layer
Service-point addressing:-
Computers often run several programs at the same time.
For this reason, source-to-destination delivery means delivery not only from one computer to the next
but also from a specific process (running program) on one computer to a specific process on the other.
The transport layer header must therefore include a type of address called a service-point address (or port address).
The network layer gets each packet to the correct computer; the transport layer gets the entire message to the correct process on that computer.

## Slide 45: Responsibilities of Layer 4: Transport Layer
2. Segmentation and reassembly:-
A message is divided into transmittable segments, with each segment containing a sequence number.
These numbers enable the transport layer to reassemble the message correctly upon arriving at the destination and to identify and replace packets that were lost in transmission.
Flow control:-
Like the data link layer, the transport layer is responsible for flow control.
However, flow control at this layer is performed end to end rather than across a single link.

## Slide 46: Responsibilities of Layer 4: Transport Layer
Error control:-
Like the data link layer, the transport layer is responsible for error control.
However, error control at this layer is performed process-to-process rather than across a single link.
The sending transport layer makes sure that the entire message arrives at the receiving transport layer without error (damage, loss, or duplication).
Error correction is usually achieved through retransmission.
Connection control:-
The transport layer can be either connectionless or connection-oriented.

## Slide 47: Responsibilities of Layer 4: Transport Layer
Connectionless
The transport layer treats each segment as an independent packet and delivers it to the transport layer at the destination machine.
B. Connection-oriented
The transport layer makes a connection with the transport layer at the destination machine first before delivering the packets.
After all the data are transferred, the connection is terminated.

## Slide 48: Layer 3: Network Layer
Defines end-to-end delivery of packets or source-to-destination delivery of a packet, possibly across multiple networks
Defines how routing works and how routes are learned so that the packets can be delivered.
The network layer ensures that each packet gets from its point of origin to its final destination
The network layer also defines how to fragment a packet into smaller packets to accommodate different media.
The routers operate at Layer 3.
Examples :- IP, IPX, AppleTalk.

## Slide 49: Layer 2: Data Link Layer
The data link layer provides access to the networking media and physical transmission across the media and this enables the data to locate its intended destination on a network.
The data link layer provides reliable transit of data across a physical link by using the Media Access Control (MAC) addresses.
The data link layer uses the MAC address to define a hardware or data link address in order for multiple stations to share the same medium and still uniquely identify each other.
Examples :
Ethernet, Frame Relay, FDDI
Notes: FDDI(Fiber Distributed Data Interface) –is a network standard that uses fiber optic connections in a local area network(LAN)
That can extend in range up to 200km (124 miles). The FDDI protocol is based on the token ring protocol. A FDDI LAN can support thousands of users

## Slide 50: Responsibilities of Layer 2: Data Link Layer
Framing.
The data link layer divides the stream of bits received from the network layer into manageable data units called frames.
2. Physical addressing.
If frames are to be distributed to different systems on the network,
the data link layer adds a header to the frame to define the sender and/or receiver of the frame.
If the frame is intended for a system outside the sender‘s network,
the receiver address is the address of the device that connects the network to the next one.
Notes: FDDI(Fiber Distributed Data Interface) –is a network standard that uses fiber optic connections in a local area network(LAN)
That can extend in range up to 200km (124 miles). The FDDI protocol is based on the token ring protocol. A FDDI LAN can support thousands of users

## Slide 51: Responsibilities of Layer 2: Data Link Layer
Flow control.
If the rate at which the data are absorbed by the receiver is less than the rate at which data are produced in the sender,
the data link layer imposes a flow control mechanism to avoid overwhelming the receiver.
4. Error control.
The data link layer adds reliability to the physical layer by adding mechanisms to detect and retransmit damaged or lost frames.
It also uses a mechanism to recognize duplicate frames.
Error control is normally achieved through a trailer added to the end of the frame.
Notes: FDDI(Fiber Distributed Data Interface) –is a network standard that uses fiber optic connections in a local area network(LAN)
That can extend in range up to 200km (124 miles). The FDDI protocol is based on the token ring protocol. A FDDI LAN can support thousands of users

## Slide 52: Responsibilities of Layer 2: Data Link Layer
5. Access control.
When two or more devices are connected to the same link,
the data link layer protocols are necessary to determine which device has control over the link at any given time.
Notes: FDDI(Fiber Distributed Data Interface) –is a network standard that uses fiber optic connections in a local area network(LAN)
That can extend in range up to 200km (124 miles). The FDDI protocol is based on the token ring protocol. A FDDI LAN can support thousands of users

## Slide 53: Layer 1: Physical Layer
The physical layer deals with the physical characteristics of the transmission medium.
It defines
Mechanical: the size and shape of the network connector, how many pins does the network connector has and what each pin is used for
Electrical: how many volts represent a 1 and how many a 0
Timing: how many nanoseconds a bit lasts whether communication is one way or in both directions simultaneously
Such characteristics as voltage levels, timing of voltage changes, physical data rates, maximum transmission distances, physical connectors, and other similar attributes are defined by physical layer specifications.
Examples :- EIA/TIA-232, RJ45, BNC.

## Slide 55: 1.7 TCP/IP Reference Model
TCP/IP Reference Model is a four-layered suite of communication protocols.
It is named after the two main protocols that are used in the model,
namely, TCP TCP/IP stands for Transmission Control Protocol / Internet Protocol
It was developed by the DoD (Department of Defence) in the 1960s as a model able to withstand intense military attack and not fail.
Data transmission was possible to any destination on the network under any circumstances.
Standardized in 1981, the TCP/IP model is now the standard on which the Internet is based.

## Slide 56: 1.7 TCP/IP Reference Model------
It has four layers
There are similarities and differences between the TCP/IP model and the seven layer OSI model.

## Slide 57: 1. TCP/IP Application Layer
Ensures that the data is properly packaged before being passed on.
Handles high-level protocols, representation, encoding, and dialog control.
There are lots of protocols defined at this layer:
  Simple Network Management Protocol (SNMP) – allows network managers to manage configurations, statistics, performance, and security.
  Domain Name System (DNS) – used to translate domain names into IP addresses.

## Slide 58: 1. TCP/IP Application Layer------
Has protocols to support file transfer, e-mail, and remote login.
File Transfer:
Trivial File Transfer Protocol (TFTP)
Unreliable, connectionless User Datagram Protocol (UDP) service used to transfer configuration files, Cisco IOS images, and to transfer files in a LAN.
2. File Transfer Protocol (FTP)
Reliable, connection-oriented service that uses TCP to transfer files between systems
3. Network File System (NFS)
Allows file access to a remote storage device such as a hard disk

## Slide 59: 1. TCP/IP Application Layer------
E-mail:
Simple Mail Transfer Protocol (SMTP)
Administers the transmission of plain text e-mail between email servers.
2. Post Office Protocol (POP3) and IMAP4
Handles email transfer between a mail server and client machine
2. Remote Access:
Telnet
A protocol that remotely access a computer, enabling a user to log into an Internet host and execute commands.
A Telnet client is called a local host. A Telnet server is called a remote host.

## Slide 60: 2. TCP/IP Transport Layer
Provides a logical connection between a source host and a destination host.
Transport Layer protocols segment and reassemble data sent by applications, into the same data stream, between end points.
Provides end-to-end control and reliability as data travels through the cloud, accomplished through:
  sequence numbers, acknowledgments and sliding windows.

## Slide 61: 2. TCP/IP Transport Layer-------
Transport
I just sent #10
I just received #10
Now I need #11
This shows sequence numbers and acknowledgements.

## Slide 62: 2. TCP/IP Transport Layer-------
Transport
I just sent #11, 12 and 13
I just received #12
Now I need #13
This indicates that packet 13 either did not arrive, or arrived with errors, and needs retransmission.
Sliding Windows

## Slide 63: 2. TCP/IP Transport Layer-------
Transport
I just sent #13 and 14
I just received #14
Now I need #15
The sliding window has worked as the last packet sent has arrived.
Sliding Windows

## Slide 64: 2. TCP/IP Transport Layer-------
The only Transport layer protocols are TCP and UDP.
  1. Transmission Control Protocol (TCP)
    Connection-oriented protocol
    End-to-end operation
    Flow control – sliding windows
    Reliability–sequence numbers and acknowledgments
  2. User Datagram Protocol (UDP)
    Connectionless
    Unreliable (no acknowledgments or error checking)
Transport

## Slide 65: 3. TCP/IP Internet Layer
Two purposes are - determining the best path and packet-switching.
No error checking or correction
Protocols:
  Internet Protocol (IP) - connectionless, best-effort delivery routing of packets; determines best path to destination
  Internet Control Message Protocol (ICMP) – control and messaging
  Address Resolution Protocol (ARP) - determines the MAC address, for a known IP address.
  Reverse Address Resolution Protocol (RARP) - determines the IP address for a known MAC address.
Internet

## Slide 66: 4. TCP/IP Network Access Layer
Allows an IP packet to make a physical link to the network media
Maps IP addresses to MAC addresses
Encapsulates IP packets into frames
Drivers for modem cards, and other devices operate at the network access layer.
Serial Line Internet Protocol (SLIP) and Point-to-Point Protocol (PPP) provide network access.
ARP and RARP also work at this layer.
Network Access
Note: This layer is not defined by TCP/IP.

## Slide 67: 1.7.1 Comparing TCP/IP and OSI
OSI Model
TCP/IP Model
Application
Network Access
Internet
Transport
Application
7
1
2
3
4
5
6
Physical
Data Link
Network
Transport
Session
Presentation
Application Layers
Data Flow Layers

## Slide 68: 1.7.1 Comparing TCP/IP and OSI------
Similarities
OSI and the TCP/IP model have a layered architecture and provide almost the same functionalities.
Both have application layers, though they include different services.
Both have comparable transport and network layers.
Both use packet-switched instead of circuit-switched technology.

## Slide 69: 1.7.1 Comparing TCP/IP and OSI------

## Slide 70: 1.7.2 Ethernet and TCP/IP
Ethernet & TCP/IP are the most omnipresent LAN protocols, and are often used together.
Data Link Layer
Physical Layer
Network Layer
Session Layer
Transport Layer
Presentation Layer
Application Layer
TCP/IP
Ethernet

## Slide 71: 1.8 Network and System Administration
Network and System Administration involves managing and
maintaining computer networks and systems to
ensure their optimal performance, security, and availability.
Network and System Administration is crucial for businesses and
organizations to maintain productivity,
secure sensitive information, and support digital infrastructure.
Effective administration helps prevent disruptions and ensures a smooth user experience.
Network and system administration is a branch of engineering,
that concerns the operational management of human–computer systems.
It is unusual as an engineering discipline in that it addresses both the
technology of computer systems and the
users of the technology on an equal basis.

## Slide 72: 1.8 Network and System Administration --------
It is about putting together a network of computers
(workstations, PCs and supercomputers),
getting them running and then keeping them running in spite of the
activities of users who tend to cause the system to fail.
Network and system administration addresses both the
technology of computer systems and
the users of the technology on an equal basis.
It is an organized collaboration between humans and
computers to solve a problem or provide a service.
A key roles to build hardware configuration and to configure software systems

## Slide 73: 1.8 Network and System Administration --------
Is network and system administration management or engineering?
Network and system administration is typically considered more of an engineering discipline rather than a management one.
Here’s why:
Technical Focus:
Network and system administrators primarily deal with the technical aspects of managing and maintaining IT infrastructure.
This includes configuring networks, setting up servers,
installing and maintaining software,
troubleshooting technical issues, and
IT INFRAS ensuring systems are secure and operational.
Notes: IT infrastructure encompasses the foundational components and resources that support the operation and management of
IT services and systems within an organization. It includes both physical and virtual elements.

## Slide 74: 1.8 Network and System Administration --------
2. Engineering Tasks:
Administrators engage in tasks that are rooted in engineering principles,
such as designing network layouts, selecting and
integrating hardware and software components,
optimizing system performance, and implementing security measures.
3. Skill Requirements:
The role requires deep technical knowledge and skills in areas like
networking protocols, server administration, virtualization,
cloud computing, cybersecurity, and more.
These technical competencies are typically associated with engineering disciplines.

## Slide 75: 1.8 Network and System Administration --------
While network and system administrators may have
some management responsibilities, such as
overseeing the day-to-day operation of IT systems,
coordinating with other departments, and managing user access
and permissions, their core activities and expertise are
centered around engineering and technical implementation
rather than managerial decision-making.
Therefore, network and system administration is more
accurately categorized under engineering within the broader
field of IT and computer science disciplines.

## Slide 76: 1.8.1 System Administration
System Administration is the
design, installation, configuration, operation, and
support of servers to support the operation
need of information technology infrastructure of an organization
Generally it is the
planning,
installing, and
maintaining computer systems involving
servers and clients that works together in a network environment
using operating system like Windows Server or Linux platform.

## Slide 77: 1.8.1 System Administration--------
System Administration refers to the management of one or more hardware and software systems.
The task is performed by a system administrator who
monitors system health,
monitor and allocates system resources like disk space,
performs backups, provides user access,
manages user accounts,
monitors system security and
performs many other functions

## Slide 78: 1.8.1 System Administration--------
System administration refers to the management, maintenance, and operation of computer systems and networks within an organization.
It involves a range of tasks and responsibilities aimed at
ensuring that IT infrastructure is running smoothly, securely, and
efficiently to support the organization's operations.
Here are key aspects of system administration:
1. System Configuration and Deployment:
Hardware Setup:
Installing and configuring servers, network devices (routers, switches),
storage systems, and other hardware components
necessary for the organization's IT infrastructure.

## Slide 79: 1.8.1 System Administration--------
B. Software Installation:
Deploying and configuring operating systems (such as
Windows Server, Linux distributions),
applications (like database management systems, web servers),
and software updates.
2. System Monitoring and Performance Optimization:
Monitoring:
Continuously monitoring system performance, resource usage (CPU, memory, disk space), and network traffic to identify bottlenecks, trends, and potential issues.
Performance Optimization:
Implementing optimizations and tuning configurations to improve system performance, reliability, and efficiency.

## Slide 80: 1.8.1 System Administration--------
3. Security Management:
Access Control:
Managing user accounts, permissions, and access controls to ensure only
authorized personnel have appropriate access to systems and data.
Security Measures:
Implementing and maintaining security measures such as firewalls,
intrusion detection/prevention systems (IDS/IPS),
antivirus software, encryption, and vulnerability management.
4. Backup and Recovery:
Backup Strategies:
Developing and implementing backup policies and procedures to regularly
back up critical data and systems to prevent data loss in case of
hardware failure, accidental deletion, or disaster.

## Slide 81: 1.8.1 System Administration--------
Disaster Recovery:
Planning and testing disaster recovery procedures to
minimize downtime and restore operations swiftly in
the event of a catastrophic failure or disaster.
5. Troubleshooting and Technical Support:
Issue Resolution:
Responding to and resolving technical issues and incidents
reported by users or identified through monitoring systems.
Technical Support:
Providing technical support and assistance to users, helping them
troubleshoot and resolve IT-related problems effectively.

## Slide 82: 1.8.1 System Administration--------
6. Documentation and Compliance:
Documentation:
Maintaining detailed documentation of system configurations, procedures, policies, network diagrams, and troubleshooting steps to ensure clarity and continuity in system management.
Compliance:
Ensuring systems and operations comply with organizational policies,
industry regulations, and legal requirements related to data protection and security.
7. Automation and Scripting:
Automation:
Implementing automation tools and scripts (using scripting languages like
PowerShell, Python, Bash) to streamline repetitive tasks,
improve efficiency, and reduce human error in system administration.

## Slide 83: 1.8.2 System Administrator
A System Administrator (often abbreviated as SysAdmin) is an
IT/Computer Science professional responsible for
managing, maintaining, and
supporting computer systems and networks within an organization.
Their primary goal is to ensure that IT infrastructure runs
smoothly, efficiently, and securely to support the
organization's operations.
Responsibilities of System Administrator:
1. System Configuration and Installation:
  Setting up and configuring servers, workstations, and network devices.
  Installing and updating operating systems and software applications.

## Slide 84: 1.8.2 System Administrator------
2. Maintenance and Monitoring:
  Continuously monitoring system performance, including CPU, memory, and storage usage.
  Performing routine maintenance tasks like applying patches and updates.
3. User Management:
  Creating and managing user accounts, permissions, and access controls.
  Providing technical support to users and resolving issues.
4. Security Management:
  Implementing security protocols, firewalls, and antivirus solutions to protect systems.
  Conducting regular security audits and vulnerability assessments.

## Slide 85: 1.8.2 System Administrator-----
5. Backup and Recovery:
  Developing and implementing backup strategies to safeguard data.
  Ensuring disaster recovery plans are in place and tested regularly.
6. Troubleshooting and Support:
  Diagnosing and resolving hardware and software issues.
  Providing support for various IT-related queries and problems.
7. Documentation:
  Maintaining documentation of system configurations, processes, and procedures.
  Keeping records of incidents and resolutions for future reference.
8. Automation:
  Utilizing scripts and automation tools to streamline routine tasks and improve efficiency.

## Slide 86: 1.8.2 System Administrator-(Skills and Qualifications):
Technical Expertise:
Proficiency in operating systems (Windows Server, Linux/Unix), networking protocols, virtualization technologies, cloud computing platforms, and IT infrastructure components.
B. Problem-Solving Abilities:
Strong analytical and problem-solving skills to diagnose and resolve complex technical issues.
C. Communication Skills:
Effective communication skills to interact with users, stakeholders, and other IT teams, as well as document procedures and technical information clearly.

## Slide 87: 1.8.2 System Administrator-(Skills and Qualifications):
D. Security Awareness:
Understanding of cybersecurity principles, best practices, and techniques to protect systems and data from evolving threats.
E. Adaptability and Learning:
Ability to adapt to new technologies, learn quickly, and stay updated with industry trends and advancements in system administration.

## Slide 88: 1.8.2 System Administrator-(Career Paths and Specializations):
System administrators can specialize in various areas such as:
A. Network Administration:
Focused on managing and optimizing network infrastructure, including routers, switches, and VPNs.
B. Database Administration:
Specializing in the management and maintenance of databases, ensuring data integrity, security, and availability.
C. Cloud Administration:
Managing cloud services and environments (like AWS, Azure, Google Cloud) for scalability, performance, and cost-efficiency.

## Slide 89: 1.8.2 System Administrator-(Career Paths and Specializations):
D. Security Administration:
Specializing in cybersecurity measures, incident response, and compliance within IT environments.
Note:
In summary, system administration is essential for maintaining the functionality, security, and efficiency of IT systems and networks.
It requires a blend of technical expertise, problem-solving skills, and proactive management to support the needs and objectives of organizations across various industries.

## Slide 90: 1.8.3 System Administration Challenges
System administration comes with a variety of challenges, including:
Security Threats:
Constantly evolving cyber threats necessitate robust security measures and ongoing monitoring.
2. Downtime Management:
Ensuring high availability and minimizing system downtime are critical for maintaining business operations.
3. User Account Management:
Managing user accounts, permissions, and addressing user-related issues can be time-consuming and complex.

## Slide 91: 1.8.3 System Administration Challenges-----
4. Backup and Disaster Recovery:
Implementing effective backup solutions and disaster recovery plans to prevent data loss is essential.
5. Compliance and Regulations:
Adhering to industry standards and regulations can be complicated and requires regular audits.
6. Software and Hardware Updates:
Keeping systems updated while minimizing disruptions can be a significant challenge.
7. Documentation:
Maintaining accurate and comprehensive documentation is crucial for troubleshooting and onboarding but is often neglected.

## Slide 92: 1.8.3 System Administration Challenges-----
8. Capacity Planning:
Anticipating future resource needs and scaling infrastructure effectively is necessary to avoid performance bottlenecks.
9. Change Management:
Implementing changes without affecting system stability requires careful planning and communication.
10. Skill Development:
Rapid technological advancements mean sysadmins must continuously update their skills and knowledge.

## Slide 93: 1.8.3 System Administration Challenges-----
11. Resource Constraints:
Limited budgets and staffing can make it difficult to address all system administration challenges effectively.
12. Interdepartmental Coordination:
Working with different departments can lead to misunderstandings and conflicting priorities.

## Slide 94: 2. Network Administration
Network administration involves managing and maintaining an organization's computer networks to ensure they operate efficiently and securely.
It encompasses a variety of tasks, including:
Network Configuration:
Setting up and configuring network hardware (like routers,
switches, and firewalls) and software to facilitate
communication between devices.
2. Monitoring and Performance Management:
Continuously monitoring network performance to identify and
resolve issues, ensuring optimal speed and reliability.

## Slide 95: 2. Network Administration -------
3. Security Management:
Implementing security measures, such as firewalls,
intrusion detection systems, and VPNs, to protect the network from unauthorized access and attacks.
4. Troubleshooting:
Diagnosing and resolving network problems, including connectivity issues, slow performance, and hardware failures.
5. User Management:
Managing user accounts and permissions, ensuring that users have appropriate access to network resources.

## Slide 96: 2. Network Administration -------
6. Network Documentation:
Maintaining accurate documentation of the network configuration,
policies, and procedures for troubleshooting and future reference.
7. Backup and Recovery:
Implementing backup solutions for network configurations and
ensuring recovery plans are in place in case of network failures.
8. Capacity Planning:
Assessing current network usage and forecasting future needs to
ensure the network can handle increased traffic.

## Slide 97: 2. Network Administration -------
9. Software Updates and Patch Management:
Keeping network software up-to-date to address vulnerabilities and
improve functionality.
10. Collaboration with Other IT Teams:
Working closely with system administrators, security teams, and other IT staff to ensure seamless integration and operation of the overall IT infrastructure.
Network administrators play a crucial role in maintaining the integrity,
security, and performance of an organization’s network,
which is vital for overall business operations.
11. Network Design and Architecture:
Planning and designing the network layout to ensure it meets organizational needs, including considerations for scalability and redundancy.

## Slide 98: 2. Network Administration------
12. Network Upgrades:
Evaluating and implementing new technologies, such as
upgrading bandwidth or integrating new hardware to
improve network performance.
13. Virtualization:
Managing virtual networks and environments, including setting up
virtual LANs (VLANs) to segment network traffic.
14. Remote Access Management:
Configuring and maintaining secure remote access solutions,
such as VPNs, to support remote work and ensure secure connections.

## Slide 99: 2. Network Administration------
15. Policy Development:
Creating and enforcing network usage policies to guide user behavior and ensure compliance with security standards.
16. Vendor Management:
Collaborating with vendors and service providers for equipment procurement, maintenance, and support services.
Incident Response:
Developing and executing incident response plans to address security breaches or network failures quickly.
Training and Support:
Providing training and support to users regarding network usage, best practices, and troubleshooting basic issues.

## Slide 100: Network Administration Skills
To excel in network administration, a combination of technical, analytical, and interpersonal skills is essential.
Here are the key skills required:
A. Technical Skills
Networking Protocols:
In-depth knowledge of protocols such as TCP/IP, DNS, DHCP, and routing protocols (e.g., OSPF, BGP).
2. Network Hardware:
Familiarity with routers, switches, firewalls, and access points, including configuration and troubleshooting.

## Slide 101: Network Administration Skills---
3. Network Security:
Understanding of cybersecurity principles, including firewalls, VPNs, intrusion detection/prevention systems, and security policies.
4. Operating Systems:
Proficiency in various operating systems, especially Windows Server, Linux, and UNIX.
5. Network Monitoring Tools:
Experience with tools like Wireshark, Nagios, SolarWinds, or PRTG for monitoring and managing network performance.

## Slide 102: Network Administration Skills---
6. Virtualization:
Knowledge of virtualization technologies (e.g., VMware, Hyper-V) and managing virtual networks.
7. Scripting and Automation:
Basic scripting skills (e.g., Python, PowerShell) to automate tasks and improve efficiency.
8. Troubleshooting:
Strong diagnostic skills to identify and resolve network issues quickly.

## Slide 103: Network Administration Skills---
B. Analytical Skills
Problem-Solving:
Ability to analyze complex problems and develop effective solutions.
2. Capacity Planning:
Skills in forecasting network needs and scaling resources accordingly.
3. Performance Analysis:
Ability to assess network performance metrics and
identify areas for improvement.

## Slide 104: Network Administration Skills---
C. Interpersonal Skills
Communication:
Strong verbal and written communication skills to collaborate with team members and explain technical concepts to non-technical users.
2. Team Collaboration:
Ability to work effectively within a team and collaborate with other IT departments.
3. User Support:
Skills in providing support and training to users on network-related issues and best practices.

## Slide 105: Network Administration Skills---
D. Organizational Skills
Documentation:
Ability to maintain clear and accurate documentation of network configurations, policies, and procedures.
2. Project Management:
Skills in planning and managing network projects, including upgrades and implementations.

## Slide 106: Network Administration Skills---
E. Continuous Learning
1. Adaptability:
Willingness to stay current with evolving technologies and trends in networking.
2. Certifications:
Earning relevant certifications (e.g., Cisco CCNA, CompTIA Network+, Juniper JNCIA) can validate expertise and enhance career prospects.
Conclusion
A successful network administrator combines these technical and soft skills to manage complex network environments effectively, ensuring security, performance, and reliability.
Continuous learning and adaptation are crucial in this ever-evolving field.

## Slide 107: Carrier path for Network Administration
A career in network administration offers various paths for growth and specialization.
Here's a typical career trajectory, along with potential roles and the skills or certifications that may help you advance:
A. Entry-Level Positions
Help Desk Technician:
Responsibilities:
Provide technical support, troubleshoot user issues, and assist with basic network problems.
Skills/Certifications:
Customer service skills, CompTIA A+, basic networking knowledge.

## Slide 108: Carrier path for Network Administration--------
Network Support Technician:
Responsibilities:
Assist with network maintenance, monitor network performance, and help implement solutions.
Skills/Certifications:
CompTIA Network+, familiarity with network monitoring tools.
B. Mid-Level Positions
Network Administrator:
Responsibilities:
Manage and maintain networks, configure hardware, implement security measures, and troubleshoot issues.
Skills/Certifications:
CCNA (Cisco Certified Network Associate), strong knowledge of network protocols and hardware.

## Slide 109: Carrier path for Network Administration-------
Systems Administrator:
Responsibilities:
Oversee both networks and server environments, manage user accounts, and ensure system security.
Skills/Certifications:
Microsoft Certified: Azure Administrator, Linux certifications (e.g., LPIC).
Network Analyst:
Responsibilities:
Analyze network performance, design network solutions, and assist in capacity planning.
Skills/Certifications:
Analytical skills, familiarity with network design tools, CCNP (Cisco Certified Network Professional).

## Slide 110: Carrier path for Network Administration-------
C. Advanced Positions
Network Engineer:
Responsibilities:
Design and implement complex network solutions, optimize performance, and ensure network security.
Skills/Certifications:
CCNP, experience with network architecture and advanced routing/switching.
Network Security Specialist:
Responsibilities:
Focus on network security measures, conduct vulnerability assessments, and respond to security incidents.

## Slide 111: Carrier path for Network Administration-------
C. Advanced Positions
Network Engineer:
Responsibilities:
Design and implement complex network solutions, optimize performance, and ensure network security.
Skills/Certifications:
CCNP, experience with network architecture and advanced routing/switching.
Network Security Specialist:
Responsibilities:
Focus on network security measures, conduct vulnerability assessments, and respond to security incidents.

## Slide 112: Carrier path for Network Administration-------
  Skills/Certifications:
  CISSP (Certified Information Systems Security Professional), CEH (Certified Ethical Hacker).
Cloud Network Architect:
Responsibilities:
Design and implement networking solutions in cloud environments, manage hybrid and multi-cloud networks.
Skills/Certifications:
AWS Certified Solutions Architect, Google Cloud Professional Cloud Architect.

## Slide 113: Carrier path for Network Administration-------
D. Leadership and Specialized Roles
IT Manager/Director:
Responsibilities:
Oversee IT operations, including network administration, system management, and team leadership.
Skills/Certifications:
Leadership skills, project management experience, ITIL certification.
Chief Information Officer (CIO):
Responsibilities:
Set the strategic direction for IT, including networking and infrastructure, and align IT with business goals.
Skills/Certifications:
Business acumen, strong leadership skills, relevant executive-level experience.

## Slide 114: Carrier path for Network Administration-------
E. Continuous Development
Certifications:
Pursuing further certifications, such as CCIE (Cisco Certified Internetwork Expert) or specialized certifications in areas like VoIP or wireless networking, can enhance your qualifications.
Training and Workshops:
Attend workshops, webinars, and training sessions to keep up with emerging technologies and trends.
Conclusion
A career in network administration can be rewarding, with opportunities for specialization and advancement.
Continuous learning and adaptation to new technologies are key to succeeding in this dynamic field.

## Slide 115: Network Monitoring and Management Tools
Network administration relies on a variety of tools and technologies to
ensure the effective management, monitoring,
and security of networks.
A. Network Monitoring and Management Tools
Network Monitoring Software:
  SolarWinds Network Performance Monitor
  Monitors network performance and provides insights into traffic patterns.
  Nagios:
  Offers monitoring of network services, hosts, and server resources.
  PRTG Network Monitor:
  Monitors network availability and performance, including bandwidth usage.

## Slide 116: Network Monitoring and Management Tools-----
2. Configuration Management Tools:
  Cisco Prime:
  Manages Cisco network devices and provides
  configuration management capabilities.
  Ansible:
  Automates network configuration and
  management tasks.
  Puppet:
  Enables automated configuration management
  across network devices.

## Slide 117: Network Monitoring and Management Tools-----
B. Security Tools
1. Firewalls:
  Cisco ASA:
  Provides advanced firewall capabilities to protect network boundaries.
  Fortinet FortiGate:
  Offers integrated security features, including firewall and intrusion prevention.
2. Intrusion Detection/Prevention Systems (IDS/IPS):
  Snort:
  An open-source network intrusion detection system for real-time traffic analysis.
  Suricata:
  Another open-source IDS/IPS for network security monitoring.

## Slide 118: Network Monitoring and Management Tools-----
VPN Solutions:
  OpenVPN:
  Open-source software for creating secure point-to-point or site-to-site connections.
  Cisco AnyConnect:
  Provides secure remote access to the network for users.
C. Network Configuration and Analysis Tools
Network Configuration Management:
NetBrain:
Provides automated network documentation and configuration management.
RANCID:
Monitors network device configurations and helps manage changes.

## Slide 119: Network Monitoring and Management Tools-----
2. Traffic Analysis Tools:
  Wireshark:
  A packet analysis tool for capturing and inspecting network traffic.
  NetFlow Analyzer:
  Analyzes traffic patterns and provides insights into bandwidth usage.
D. Network Design and Diagramming Tools
1. Network Diagramming Software:
  Microsoft Visio:
  Widely used for creating network diagrams and documentation.
  Lucidchart:
  A web-based tool for creating diagrams, including network layouts.

## Slide 120: Network Monitoring and Management Tools-----
E. Virtualization and Cloud Tools
1. Virtualization Platforms:
  VMware:
  Provides solutions for virtualizing servers and networks.
  Hyper-V:
  Microsoft’s virtualization platform for managing virtual machines.
2. Cloud Networking Solutions:
  AWS VPC:
  Amazon’s Virtual Private Cloud for managing network resources in the cloud.
  Azure Virtual Network:
  Microsoft Azure’s solution for creating private networks.

## Slide 121: Network Monitoring and Management Tools-----
F. Command-Line and Scripting Tools
1. Command-Line Interfaces (CLI):
  Familiarity with the CLI of routers and switches
  (e.g., Cisco IOS, Juniper Junos) is essential for
  configuration and troubleshooting.
2. Scripting Languages:
  Python:
  Useful for automating tasks and managing network configurations.
  Bash:
  For scripting in Unix/Linux environments.

## Slide 122: Network Monitoring and Management Tools-----
G. Performance Testing Tools
1. Network Testing Tools:
  iPerf:
  Measures network bandwidth and performance.
  PingPlotter:
  Visualizes network performance and latency over time.
H. Backup and Recovery Tools
1. Backup Solutions:
  Cisco Network Assistant:
  Assists with configuration backups for Cisco devices.
  Rsync:
  A command-line utility for efficient file backups and synchronization.

## Slide 123
System Administrator Vs Network Administrator |  | 
 | System Administrator | Network Administrator
1 | Installing, configuring, and updating software and applications... | Configuring and maintaining network hardware (routers, switches, firewalls).
2 | Monitoring system performance and troubleshooting issues. | Monitoring network performance and security.
3 | Managing user accounts and permissions | Troubleshooting network connectivity issues.
4 | Implementing security measures and backups | Implementing network security protocols.
5 | Performing system upgrades and migrations. | Managing IP addresses and DNS settings.