## Slide 1: Internet Protocol (IP) and IP Addressing
CHAPTER ONE PART TWO

## Slide 2: 1.1 Internet Protocol (IP)
It is a protocol used for communicating data across a packet-switched internetwork using the Internet Protocol Suite, also referred to as TCP/IP.
IP is the primary protocol in the Internet Layer of the Internet Protocol Suite and has the task of
delivering distinguished protocol datagrams (packets) from the
source host to the destination host solely based on their addresses.
For this purpose the Internet Protocol defines addressing methods
and structures for datagram encapsulation.
The first major version of addressing structure, now referred to as
IPv4 is still the dominant protocol of the Internet, although the successor, IPv6,
is being deployed actively worldwide (128 bits).
Notes: Internet Protocol suite (IP suite) is the standard network model and communication protocol stack used on the Internet and on most other computer networks. While other networking models exist, the IP suite is overwhelmingly the global standard for computer-to-computer communication

## Slide 3: 1.1 Internet Protocol (IP)--------
Communication at the network layer is
host-to-host (computer-to-computer);
a computer somewhere in the world needs to communicate with another computer somewhere else in the world.
Usually, computers communicate through the Internet.
The packet transmitted by the sending computer may pass through several LANs or WANs before reaching the destination computer.
For this level of communication, we need a global addressing scheme;
we use the term IP address to mean a logical address in
the network layer of the TCP/IP protocol suite.

## Slide 4: 1.2 IPv4 Addresses
An IPv4 address is a 32-bit address that uniquely and universally defines the connection of a device (for example,
a computer or a router) to the Internet.
IPv4 addresses are unique and universal.
They are unique in the sense that each address defines
one, and only one, connection to the Internet.
Two devices on the Internet can never have the same address at the same time.

## Slide 5: 1.3 Address Space
An address space is the total number of addresses used by the protocol.
If a protocol uses N bits to define an address,
the address space is 2N because each bit can have two different values
(0 or 1) and N bits can have 2N values.
IPv4 uses 32-bit addresses, which means that the address space is
232 or 4,294,967,296 (more than 4 billion).
This means that, theoretically, if there were no restrictions,
more than 4 billion devices could be connected to the Internet.
We will see shortly that the actual number is much less
because of the restrictions imposed on the addresses.

## Slide 6: 1.4 IP Address Notations
There are two prevalent notations to show an IPv4 address:
Binary notation and Dotted-decimal notation.
Binary Notation
In binary notation, the IPv4 address is displayed as 32 bits.
Each octet is often referred to as a byte.
So it is common to hear an IPv4 address referred to as a 32-bit address or a 4-byte address.
The following is an example of an IPv4 address in binary notation:
  01110101 10010101 00011101 00000010
Notes: Octet-is a group of three bits, representing any of eight possible values

## Slide 7: 1.4 IP Address Notations-----
2. Dotted-Decimal Notation
To make the IPv4 address more compact and easier to read,
Internet addresses are usually written in decimal form with a decimal point (dot) separating each decimal number.
The following is the dotted-decimal notation of the above address: 117.149.29.2
Example: Dotted-decimal notation and binary notation for an IPv4 address

## Slide 8
1. Change the following IPv4 addresses from binary notation to dotted-decimal notation.
Example 1
Solution
We replace each group of 8 bits with its equivalent decimal number and add dots for separation.

## Slide 9
2. Change the following IPv4 addresses from dotted-decimal notation to binary notation.
Example 1--------
Solution
We replace each decimal number with its binary equivalent.

## Slide 10
3. Find the error, if any, in the following IPv4 addresses.
Example 1--------
Solution
There must be no leading zero (045).
There can be no more than four numbers.
Each number needs to be less than or equal to 255.
A mixture of binary notation and dotted-decimal notation is not allowed.

## Slide 11: 1.5 Classful Addressing
Classful addressing is an early method of allocating IP addresses,
which divides the address space into distinct classes based on the
leading bits of the address.
This approach has largely been replaced by Classless Inter-Domain Routing (CIDR), but it's still useful for understanding the basic structure of IP addressing.
Network Address
The network address identifies the specific network segment
in which a device (or host) resides.
It is used by routers to direct packets toward the correct network
Network Address helps in routing packets to the appropriate network.
All devices within the same network share the same network address.

## Slide 12: 1. Network Address (Types of Network Addresses)
Routers use the host address(host ID) to determine the best path for data packets.
By examining the Network ID, routers can direct
traffic efficiently to the appropriate network segment.
1. IPv4 Address:
A 32-bit address commonly represented in decimal format (e.g., 192.168.1.1).
It includes a network portion and a host portion.
2. IPv6 Address:
128-bit address represented in hexadecimal format(e.g., 2001:0db8:85a3:0000:0000:8a2e:0370:7334).
It provides a much larger address space compared to IPv4.

## Slide 13: 1. Network Address----
3. MAC Address:
A hardware address used to identify devices on a local network.
It's a unique identifier assigned to network interfaces.
4. Public vs. Private Addresses:
Public addresses are routable on the internet, while
private addresses are used within local networks
(e.g., 192.168.x.x).

## Slide 14: 1. Host Address
A host address is a unique identifier assigned to a device (or host) on a network.
It allows the device to be recognized and communicate with other
devices within the same network or across different networks.
Device Identification:
Each device on a network must have a unique host address (Host ID) to
prevent IP address conflicts.
This ensures that data packets are delivered to the correct destination.
The concept of a host address can encompass both
IP addresses and MAC addresses, but it is primarily associated
with IP addresses in the context of networking.

## Slide 15: 1. Host Address-----
Components of a Host Address
IP Address:
Each host on a network is assigned an IP address.
This address can be static (fixed) or dynamic (assigned by a DHCP server).
In IPv4 addressing, the host address is part of the full IP address, which is typically structured as:
Network Portion:
Identifies the network itself.
Host Portion:
Identifies the specific device within that network.

## Slide 16: 1. Host Address
For example, in the IP address 192.168.1.10 with a
subnet mask of 255.255.255.0, 192.168.1
identifies the network, while 10 identifies the host.
MAC Address:
While IP addresses are used primarily for routing over networks,
MAC addresses are used at the data link layer for
communication within the same local network.
Each network interface card (NIC) has a unique MAC address,
ensuring that data packets can be directed to the correct
device on a local network.

## Slide 17: 1. Host Address (Importance of Host Addresses)
1. Unique Identification:
Host addresses allow devices to be uniquely identified,
ensuring accurate communication and data transfer.
2. Routing and Switching:
Routers use host addresses to determine where to forward packets, while switches use MAC addresses to direct data to the correct devices on a local network.
3. Network Management:
Administrators use host addresses for monitoring network activity,
managing resources, and troubleshooting connectivity issues.
.

## Slide 18: 1.5 Classful Addressing-------
This architecture is called classful addressing.
In classful addressing, the address space is divided into five classes:
A, B, C, D, and E.
Each class occupies some part of the address space.

## Slide 19: 1.5 Classful Addressing-------
A. Class A:
Range: 0.0.0.0 to 127.255.255.255
Leading Bits: 0
Default Subnet Mask: 255.0.0.0
Hosts: Supports a large number of hosts (over 16 million).
This class is for large networks and has 8 bits for network and 24 bits for hosts.
2. Class B:
Range: 128.0.0.0 to 191.255.255.255
Leading Bits: 10
Default Subnet Mask: 255.255.0.0
Hosts: Supports about 65,000 hosts.
This class is for medium networks and has 16 bits for network and 16 bits for hosts.

## Slide 20: 1.5 Classful Addressing-------
3. Class C:
Range: 192.0.0.0 to 223.255.255.255
Leading Bits: 110
Default Subnet Mask: 255.255.255.0
Hosts: Supports up to 254 hosts.
This class is for smaller networks and has 24 bits for network and 8 bits for hosts.
4. Class D:
Range: 224.0.0.0 to 239.255.255.255
Leading Bits: 1110
Purpose: Used for multicast groups.

## Slide 21: 1.5 Classful Addressing-------
5. Class E:
Range: 240.0.0.0 to 255.255.255.255
Leading Bits: 1111
Purpose: Reserved for experimental use.

## Slide 22
Find the class of each address.
a. 00000001 00001011 00001011 11101111
b. 11000001 10000011 00011011 11111111
c. 14.23.120.8
d. 252.5.15.111
Example 2
Solution
a. The first bit is 0. This is a class A address.
b. The first 2 bits are 1; the third bit is 0. This is a class C address.
c. The first byte is 14; the class is A.
d. The first byte is 252; the class is E.

## Slide 23
Find the class of each address.
a. 00000001 00001011 00001011 11101111
b. 11000001 10000011 00011011 11111111
c. 14.23.120.8
d. 252.5.15.111
Activity
Solution
a. The first bit is 0. This is a class A address.
b. The first 2 bits are 1; the third bit is 0. This is a class C address.
c. The first byte is 14; the class is A.
d. The first byte is 252; the class is E.

## Slide 24
Activity
Identify the class of each IP address below:
10.15.34.56 2. 145.23.45.67 3. 200.75.12.34 4. 225.5.6.7
5. 250.255.255.255
10.15.34.56
Class A (First octet: 10, which is in the range 1–127)
2. 145.23.45.67
Class B (First octet: 145, which is in the range 128–191)
3. 200.75.12.34
Class C (First octet: 200, which is in the range 192–223)
4. 225.5.6.7
Class D (First octet: 225, which is in the range 224–239)
5. 250.255.255.255
Class E (First octet: 250, which is in the range 240–255)

## Slide 25: 1.5.1 Address Blocks
Address blocks are ranges of IP addresses that are allocated to organizations or ISPs.
These blocks can be divided into subnets for efficient management and use.
Here's how it works:
1. CIDR Notation:
Instead of relying solely on classful addressing, CIDR
(Classless Inter-Domain Routing) allows for
flexible subnetting and the allocation of address blocks.
CIDR notation combines the IP address with a subnet mask,
e.g., 192.168.1.0/24, where "/24" indicates the number
of bits used for the network part.
Notes: 2

## Slide 26: 1.5.1 Classes and Blocks
2. Allocation:
Blocks are often allocated based on the needs of an organization, allowing for varying sizes.
For example, an organization needing a small number of addresses
might receive a /28 block (16 addresses), while a
larger organization might get a /16 block (65,536 addresses).
3. Subnetting:
Organizations can further divide their allocated blocks into smaller
subnets to optimize address usage, improve security, and
enhance network performance.
This helps Efficient Use of Address Space
Notes: 2

## Slide 27: 1.5.1 Classes and Blocks
4. Supernetting:
This is the practice of aggregating several smaller blocks into a
larger one to simplify routing tables.
Notes: 2

## Slide 28: 1.6 Subnet Mask
A subnet mask is a 32-bit number used in networking to divide an
IP address into a network portion and a host portion.
It plays a crucial role in determining how many devices can exist
within a network and how routing takes place.
Structure of a Subnet Mask
Binary Format:
A subnet mask is expressed in binary, with a series of contiguous ones (1s) followed by contiguous zeros (0s).
The ones indicate the network portion, and the zeros indicate the host portion.
Example:
A subnet mask of 255.255.255.0 in binary is 11111111.11111111.11111111.00000000.

## Slide 29: 1.6 Subnet Mask-----
2. CIDR Notation:
Subnet masks can also be expressed in
Classless Inter-Domain Routing (CIDR) notation,
which uses a slash (/) followed by the number of bits set to one.
Example:
255.255.255.0 is represented as /24 because the first 24 bits are ones.

## Slide 30: How Subnet Masks Work?
A subnet mask is used to divide an IP network into smaller subnetworks (subnets).
It helps a device (such as a router or computer) to determine whether an
IP address belongs to the same network or needs to be
routed to another network.
A subnet mask is a 32-bit number that looks similar to an IP address.
It consists of two parts:
The network portion, which is used to identify the network.
The host portion, which identifies individual devices (hosts) within that network.

## Slide 31: How Subnet Masks Work?-----
Subnet Mask Structure
Subnet masks consist of 1s in the network portion and 0s in the host portion.
The 1s tell the device which bits of the IP address correspond to the
network, and the 0s tell it which bits correspond to the host.
For example:
IP Address: 192.168.1.0
Subnet Mask: 255.255.255.0
Network Address Calculation:
Result: 11000000.10101000.00000001.00000000 (which is 192.168.1.0)

## Slide 32: How Subnet Masks Work?-----
Determining Hosts in a Subnet:
When you create a subnet, you divide a network into smaller, more manageable segments.
Each subnet has a set of IP addresses available for assignment to hosts (e.g., computers, printers, routers, etc.).
However, not every IP address in the subnet can be used by a host.
Certain addresses are reserved for special purposes.
To determine how many usable host IP addresses are available within a subnet, you need to know:

## Slide 33: How Subnet Masks Work?-----
The subnet mask (or CIDR notation).
The network address and broadcast address for the subnet.
The number of host bits in the subnet.
Let's break down how to determine the number of usable host addresses in a subnet:
Step-by-Step Process for Determining Hosts
Identify the Subnet Mask:
A subnet mask tells you how many bits are allocated for the
network portion of the address (1s) and how many are
available for hosts (0s).

## Slide 34: How Subnet Masks Work?-----
For example:
  Subnet Mask (decimal): 255.255.255.0
  Subnet Mask (CIDR notation): /24
This means that the first 24 bits are used for the network portion, and the remaining 8 bits are for host addresses.
2. Calculate the Number of Host Bits:
The number of host bits is the total number of bits in the IP address
(32 for IPv4) minus the number of bits used for the
network (as specified by the subnet mask).

## Slide 35: How Subnet Masks Work?-----
For example, if the subnet mask is /24:
  Total bits in IPv4 = 32 bits.
  Network bits = 24 (because the subnet mask is /24).
  Host bits = 32 - 24 = 8 host bits.
Calculate the Total Number of IP Addresses:
The number of total addresses in a subnet is determined by the number of host bits. The formula is:
Total IP addresses=2host bits
So for a /24 subnet (where there are 8 host bits):
Total IP addresses=28=256 total addresses

## Slide 36: How Subnet Masks Work?-----
4. Subtract Reserved Addresses:
In each subnet, two IP addresses are reserved:
The network address (the first address in the subnet).
The broadcast address (the last address in the subnet).
These cannot be assigned to hosts,
so you subtract 2 addresses from the
total count to get the number of usable host IP addresses.
For a /24 subnet:
Usable IP addresses=256−2=254
Therefore, in a /24 subnet, there are 254 usable IP addresses for hosts

## Slide 37: Examples of Different Subnet Masks
Let’s look at a few examples of common subnet sizes and how to calculate the number of usable hosts.
/30 Subnet Mask (255.255.255.252)
Total IP addresses:
232−30 =22= 4 total addresses.
Usable IP addresses:
4 total addresses-2 reserved addresses (network and broadcast) = 2 usable IP addresses.
Use Case:
A /30 subnet is typically used for point-to-point links,
where only two devices need to communicate (e.g., two routers).

## Slide 38: Examples of Different Subnet Masks------
2. /29 Subnet Mask (255.255.255.248)
Total IP addresses:
Total addresses= 232−29 =23=8
Usable IP addresses:
8 total addresses - 2 reserved = 6 usable IP addresses.
Use Case:
A /29 subnet might be used in small networks, like a small office where 6 devices need IP addresses.

## Slide 39: Examples of Different Subnet Masks------
3. /24 Subnet Mask (255.255.255.0)
Total IP addresses: 232−24=28 =256 total addresses.
Usable IP addresses: 256 total addresses - 2 reserved = 254 usable IP addresses.
Use Case:
A /24 subnet is common in smaller networks, such as
home networks or small businesses.

## Slide 40: Examples of Different Subnet Masks------
4. /16 Subnet Mask (255.255.0.0)
Total IP addresses:
232−16=216=65,5362= total addresses.
Usable IP addresses:
65,536 total addresses - 2 reserved = 65,534 usable IP addresses.
Use Case:
A /16 subnet is typically used in large networks (e.g., a corporate network with many devices).

## Slide 41: Key Points to Remember

## Slide 42: Key Points to Remember
Network Address: The first address in a subnet, used to identify the network.
Broadcast Address: The last address in a subnet, used to send data to all hosts in the subnet.
Usable Addresses: The addresses between the network address and the broadcast address that can be assigned to devices (hosts).
Conclusion
To determine how many hosts can be in a subnet, you:
Calculate the number of host bits based on the subnet mask.
Use the formula 2host bits to find the total number of IP addresses in the subnet.
Subtract 2 addresses (network and broadcast) to get the number of usable IP addresses for hosts.
This process is crucial for network planning, ensuring that you allocate an appropriate number of IP addresses for each subnet without wasting address space.

## Slide 43: 1. First Address
The first address in the block can be found by setting the 32-n rightmost bits in the binary notation of the address to 0s.
Example 5: A block of addresses is granted to a small organization.
Addresses is 205.16.37.39/28. What is the first address in the block?
Solution: The binary representation of the given address is
11001101 00010000 00100101 00100111
If we set 32−28 rightmost bits to 0, we get
11001101 00010000 00100101 00100000 or 205.16.37.32

## Slide 44: 2. Last Address
The last address in the block can be found by setting the 32-n rightmost bits in the binary notation of the address to 1s.
Example 6: Find the last address for the block in Example 5.
Solution
The binary representation of the given address is
11001101 00010000 00100101 00100111
If we set 32−28 rightmost bits to 1, we get
11001101 00010000 00100101 00101111 or
205.16.37.47

## Slide 45: 3. Number of Addresses
The number of addresses in the block is the difference between the last and first address.
It can easily be found using the formula 232-n.
Example 7
Find the number of addresses in Example 5.
Solution
The value of n is 28, which means that number of addresses is 2 32−28 or 16.

## Slide 46: Number of Addresses continued
Another way to find the first address, the last address, and the number of addresses is to represent the mask as a 32-bit binary (or 8-digit hexadecimal) number.
This is particularly useful when we are writing a program to find these pieces of information. In the above example the /28 can be represented as
11111111 11111111 11111111 11110000
(twenty-eight 1s and four 0s). Find
a. The first address
b. The last address
c. The number of addresses.

## Slide 47
Solution
The first address can be found by ANDing the given addresses with the mask.
ANDing here is done bit by bit.
The result of ANDing 2 bits is 1 if both bits are 1s; the result is 0 otherwise.

## Slide 48
b. The last address can be found by ORing the given addresses with the complement of the mask.
Oring here is done bit by bit.
The result of ORing 2 bits is 0 if both bits are 0s; the result is 1 otherwise.
The complement of a number is found by changing each 1 to 0 and each 0 to 1.

## Slide 49
c. The number of addresses can be found by complementing the mask, interpreting it as a decimal number, and adding 1 to it.

## Slide 50: Network Addresses
A very important concept in IP addressing is the network address.
When an organization is given a block of addresses, the organization is free to allocate the addresses to the devices that need to be connected to the Internet.
The first address in the class, however, is normally (not always) treated as a special address.
The first address is called the network address and defines the organization network.
It defines the organization itself to the rest of the world.
The first address is the one that is used by routers to direct the message sent to the organization from the outside.

## Slide 51: The Fast Way
Before starting, you need to do is answer five simple questions:
  1. How many subnets does the chosen subnet
  mask produce?
  2. How many valid hosts per subnet are available?
  3. What are the valid subnets?
  4. What’s the broadcast address of each subnet?
  5. What are the valid hosts in each subnet?

## Slide 52: Number of Subnets
How many subnets?
  2x - 2= number of subnets. x is the number of masked bits, or the 1s.
  For example, given a class C subnet mask of 255.255.255.192, the number of ones gives us 22 = 4 subnets.
  Note that we only count the number of ones that are found in the host part of the subnet mask.
  For class C address 255.255.255.0 is the default subnet, 192=11000000 in binary, so there are only 2 ones.

## Slide 53: Number of Hosts per subnet and its valid subnets
How many hosts per subnet?
  2y – 2 = number of hosts per subnet. y is the number of unmasked bits, or the 0s. For example, in 11000000, the number of zeros gives us 26 – 2 = 62 hosts per subnet.
  You need to subtract two for the subnet address and the broadcast address, which are not valid hosts.
What are the valid subnets?
  First calculate the block size.
  256 – subnet mask = block size, or increment number.
  An example would be 256 – 192 = 64. The block size of a 192 mask is always 64.
  Second, start counting at zero in blocks of 64 until you reach the subnet mask value and these are your subnets. 0, 64, 128, 192.

## Slide 54
What’s the broadcast address for each subnet?
  Since we counted our subnets in the last section as 0, 64, 128, and 192, the broadcast address is always the number right before the next subnet.
  For example, the 0 subnet has a broadcast address of 63 because the next subnet is 64. The 64 subnet has a broadcast address of 127 because the next subnet is 128, etc.
  And remember, the broadcast of the last subnet is always 255 for Class C.
What are the valid hosts?
  Valid hosts are the numbers between the subnets, omitting all the 0s and all 1s.
  For example, if 64 is the subnet number and 127 is the broadcast address, then 65–126 is the valid host range—it’s always the numbers between the subnet address and the broadcast address. These are the addresses you assign to nodes.

## Slide 55: Activity
We’re going to subnet the network address 192.168.10.0 and subnet mask 255.255.255.224.
How many subnets?
224 is 11100000, so our equation would be 23 = 8.
2. How many hosts: 25 – 2 = 30.
3. What are the valid subnets?
    256 – 224 = 32. We just start at zero and count to the subnet mask value in blocks (increments) of 32: 0, 32, 64, 96, 128, 160, 192, 224.
4. What’s the broadcast address for each subnet?
    Always the number right before the next subnet
5. What are the valid hosts?
    The numbers between the subnet number and the broadcast address

## Slide 56: Network Naming
The process of assigning names to elements within a network,
such as devices, servers, resources, or services,
in order to facilitate easier identification and communication.
This can include naming schemes for various layers of networking, ranging from individual devices to the entire network infrastructure.
Here are some common aspects of network naming:
1. Domain Name System (DNS)
DNS is a hierarchical naming system for computers and services connected to the internet or a private network.
It translates human-readable domain names (e.g., www.example.com) into IP addresses (e.g., 192.168.1.1).

## Slide 57: Network Naming----
The network naming within DNS follows a hierarchy:
  Top-Level Domains (TLD): e.g., .com, .org, .edu.
  Second-Level Domains: e.g., example.com.
  Subdomains: e.g., mail.example.com.
Naming within DNS helps manage and direct network traffic across a global scale.
2. Host Naming
Each device in a network typically needs a unique name to identify it on the network.
Hostnames are assigned to devices to avoid confusion.
For instance:
Simple Hostnames: A computer might be named server1, printer02, etc.
FQDN (Fully Qualified Domain Name):
A host may have a full name like server1.example.com, which specifies its location in the DNS hierarchy.

## Slide 58: Network Naming-----
3. Network Identification (IP Addressing)
Numerical labels assigned to devices on a network for identification and communication.
IPv4: e.g., 192.168.1.1.
IPv6: e.g., 2001:0db8:85a3:0000:0000:8a2e:0370:7334.
While IP addresses are numeric, network devices are typically identified by more human-readable names.
4. Local Area Network (LAN) Naming
On a smaller scale, in an enterprise or home network, devices within a LAN may be named according to a specific naming convention. Examples include:
Departments: HR-Server, Marketing-PC.
Function: DB-Server, Web-Server.
Device Type: Router-01, Switch-01.
Using a naming convention helps administrators identify devices' roles and locations easily.

## Slide 59: Network Naming-----
5. Subnet Naming
In larger networks, subnets are smaller divisions of the network.
Naming conventions for subnets might include:
Subnet Name: e.g., Marketing-Subnet, Admin-Subnet.
Subnet Address: e.g., 192.168.0.0/24, indicating a network range.
6. Service Naming
Services or applications running on a network may also have specific names for identification.
For example, a web service might be named web-server01, and a database service could be db-prod01.
7. Network Devices Naming Convention
Networking devices like routers, switches, and firewalls are often given meaningful names to help identify their role and location:
Router: Core-Router-01.
Switch: Switch-Branch-02.
Firewall: FW-Edge-01.
Clear naming conventions help reduce confusion during network troubleshooting and maintenance.

## Slide 60: Network Naming-----
8. Wireless Network (SSID) Naming
Wireless networks also have names known as SSIDs (Service Set Identifiers).
An SSID identifies the network to wireless devices, and it can be named in a
way that reflects its purpose or location, such as
Corporate-WiFi, Guest-Network, or Home-WiFi.

## Slide 61: Benefits of Network Naming Conventions
Clarity and Organization:
Naming devices, services, and networks in a standardized way helps system administrators quickly understand the function and location of a resource.
2. Simplified Troubleshooting:
Consistent names help with identifying issues on specific devices or networks during troubleshooting.
3. Scalability:
A well-designed naming convention supports network growth, making it easier to add new devices and services without causing confusion.
4. Security:
Logical and transparent naming conventions can enhance security by making it easier to track and audit devices and services across a network.

## Slide 62: Considerations for Good Network Naming
Consistency:
Ensure that naming conventions are applied uniformly across the entire network.
2. Descriptive:
Choose names that clearly describe the device's function, location, or role.
3. Avoid Special Characters:
Special characters can sometimes cause issues, so it’s best to stick with alphanumeric characters and hyphens.
4. Scalability:
Plan for future growth by choosing names that will still make sense as the network expands.